# MDF and HDF fibre boards

# www.vitebskdrev.com

Within the framework of the investment project “The organization of wooden fibre boards (MF/HDF) manufacturing at the JSC “Vitebskdrev”, the program of modernization of woodworking industry enterprises is being carried out, which allows MDF/HDF fibre boards manufacturing. MDF, HDF (Customs Union Commodity Classification of Foreign Economic Activity 4411) is used while manufacturing of furniture, interior decorating, as wall panels in shopping premises and as laminate flooring (laminate). MDF, which is used while manufacturing of wardrobes, fronts with carving elements, also as a material for surface cutting, curvilinear holes and other curvilinear shapes.

The production process of MDF/HDF fibre board of medium density is presupposed to be performed on the basis of complete automated equipment of the company “IMAL Srl”, Italy.

Production capacity is 400,3 m³/day or 132 099 m³/year, including:

- laminboard (MDF/HDF) – up to 4195500 m²/year (size 1830x1220 mm);

- laminate flooring – up to 2500000 m²/year.

The size of MDF board is 1830x2440 mm, thickness is 4-40 mm, density is ≥ 650 kg/m³.

The density of HDF board will be ≥800 kg/m³.

Industrial wooden raw materials and industrial chips are raw materials for MDF/HDF manufacturing.

| 67 ton | 21,5 ton | 21,5 ton |
| --- | --- | --- |
| 38 packages | 12 packages | 12 packages |
| 82-84 m3 | 24-26 m3 | 24-26 m3 |

Fibre boards are piled in bundles wrapped with synthetic or steel straps. Bundles are formed from fibre boards of the same size, brand, type and surface.

Price thickness 16;18 mm FCA Vitebsk –170 EUR\m3 .

regarding purchase contact:

For the Republic of Belarus and CIS countries

• (+375 212) 34-09-42 – Sales manager Denis Vladimirovich Segodnik

• (+375 212) 34-21-35, 34-12-23, 34-20-53 ( fax ) – Sales and marketing department

• (+375 212) 34-12-53 ( fax ) – Sales department of joinery products

For far-abroad countries                                                               WWW.VITEBSKDREV.COM

• (+375 212) 34-06-34 (FAX)                                                            DREV@VITEBSK.BY

• (+375 212) 34-12-61